## Slide 1: Graphics Introduction Jian Zhao 2013/12/26

## Slide 2: Agenda
Graphics in Our Daily Life
What is GPU
Basic 3D Pipeline
Qualcomm Adreno Generation
Android Graphics Integration

## Slide 3
Graphics in Our Daily Life
What can we do with GPU?
What can we do with GPU in future?

## Slide 4: What we can do with GPU?
3D Games
3D/Composite UI
3D Modeling
Image/Video Processing

## Slide 5
What we can do with GPU in future?
3D Web Pages
Augmented Reality
3D User Interfaces
Mobile Navigation
3D Video/Imaging
Data Mining/Analytics
Console Quality
3D Games
Notes: HTC Sense UI

## Slide 6
What Is GPU?
What are running on GPU?
What does GPU driver do?
Why GPU is faster?

## Slide 7
MODEM
CPU(s)
GPU
Multimedia
GPS, WiFi
Etc.
Graphics Acceleration in Qualcomm Chipsets

## Slide 8: What Are Running on GPU?
*The graph is cut from NV programing guide.

## Slide 9: What Does GPU Driver Do?
API Translation
  Correctness
  Efficiency
  Shader Compiler
Scheduling and load balance
  Resource scheduling
  Load balance
    CPU and GPU
    Multi-CPU and Multi-GPU
Workaround for HW limitation or bug
Driver Model
  User mode driver: Receive application input
  Kernel mode driver: Access hardware; Global scheduler

## Slide 10: Why GPU Is Faster ?
  Execution of different stages can be parallel by different HW units
  SIMD procession
  Internal multi-thread to boost performance
    Many ALUs to support many threads to run on parallel
    Hide memory access latency and pipeline stall
  High bandwidth memory system
Parallelism!
Parallelism!
Parallelism!
 | GFLOPS | BW(GB)
9600GT (64 Sp) | 312 | 57.6
GTX 280 (240 sp) | 933 | 142

## Slide 11
Basic 3D Pipeline
How does a basic 3D pipeline look like?
How GPU works?

## Slide 12: 3D Pipeline Overview
Frame buffer
Pixel Shader
Texture Storage + Filtering
Rasterizer
Vertex Shader
Vertex Setup
CPU/
Driver
Vertices
Pixels
GPU

## Slide 13: How Does GPU Draw and Paint?
Modeling
  Use triangles as the basic brick for all geometries.
Transformation

## Slide 14: How Does GPU Draw and Paint? (cont)
Lighting
  Vertices lit (shaded) according to material properties, surface properties (normal) and light sources
  Ambient, Diffuse, Specular, Emissive.
Rasterization
blue
red
green

## Slide 15: How Does GPU Draw and Paint? (cont)
Texture
Depth Test

## Slide 16: Quiz 
How many data do we need for a vertex point?
  Position: x, y, z, w
  Color: r, g, b, a
  Texture Coordinate: u, v
  Normal: x, y, z (for lighting, reflection, etc.)
  ……

## Slide 17: Game Snapshots

## Slide 18
Qualcomm Adreno Generation
Adreno generation and capability
Adreno 3xx HW

## Slide 19: Qualcomm Adreno Generation
4 Cylinder Car Engine
V8 Car Engine
Motorcycle Engine
ADRENO 205
Moped Engine
Dirt bike Engine
ADRENO 200
ADRENO 220/5
ADRENO 320
ADRENO 305
Airplane Jet Engine
ADRENO 420
ADRENO 410
ADRENO 4-Lite
Rocket Engine
ADRENO 520
ADRENO 510
ADRENO 5-Lite
GPU Requirements will continue to Exponentially Increase over the next 5 years

## Slide 20: Adreno 3xx GPU
Adreno™ 305 GPU (450 MHz)
Same amount of ALUs as on Adreno 320
On-Chip Memory (OCMEM) For graphics, 128 KB(512K for 8x30) for fast Z, color, and stencil rendering
No 2D hardware core (8x30) but still has C2D
8x26:
Adreno305,3D core 400MHz OpenGLES1.1 - 3.0 OpenCL1.1e
Direct3D 9.3
EGL 1.4
8x25:
Adreno203, 3D core 245MHz
OpenGLES1.1 - 2.0
Direct3D 9.0c
EGL 1.4

## Slide 21: Adreno 3xx GPU(cont)
TP: Texture Pipe
400MHz
Scheduler
OGL
VTX
Thread
3D Application
OCL
Work Groups
2D
Application
Unified L2 Cache
Post TransformVertex Cache
L1 Cache
TP
Render Backend
Shader Processor
Texture
Texture
Texture data
TP
L1 Cache
TP
Render Backend
Shader Processor
Texture
Texture
Texture data
TP
L1 Cache
TP
Render Backend
Shader Processor
Texture
Texture
Texture data
TP
L1 Cache
TP
Render Backend
Shader Processor
Texture
Texture
Texture data
TP
External Memory
Color & Z
Color & Z
Color & Z
Color & Z
Pixel
Pixel
Pixel
Pixel
Pixel
Pixel
Pixel
Pixel
Vertex
Vertex
Vertex
GMEM
Vertex
Scalable “SP” Unit for A3XX Tiers
Notes: How many ALUs in a SP? simd32 (* 16 dbouble(32))

## Slide 22
Android Graphics Integration
Android Graphics stack
Adreno Graphics Driver Architecture
Adreno features overview
How to composite windows?

## Slide 23: Android Graphics Stack
    Graphics Application
Surface Flinger
EGL Wrapper
(libEGL.so)
Graphics Driver
(OpenGL ES)
Frame Buffer
ION (PMEM/ASHME)M)
KGSL
(Kernel module)
User Space
Kernel Space
MDP
GPU
Hardware
Google
OEM\3rdParty
Qualcomm
Java Level
Native Level
Java level OES/EGL Wrapper

## Slide 24: Adreno Graphics Driver Architecture

## Slide 25: Adreno Graphics Drivers
User mode drivers:
Kernel mode drivers:
Kernel Graphics System Layer(KGSL) driver
Kernel/drivers/gpu/msm/

## Slide 26: Adreno Features overview
Unified shader architecture increases efficiency of vertex and pixel shaders High degree of latency hiding with FIFOs and multithreading
Sophisticated shader support Support for branched shaders
Support for up to 16 textures in a single pass
Early rejection of nonvisible data for efficiency and performance Back-facing triangles removed before attribute processing
Hidden pixels removed before texture fetch and pixel processing
Extensive frame buffer format coverage 16 and 24-bit Z with 8-bit stencil
16 and 32-bit color
RGBA, ABGR color ordering
Wide range of texture formats supported 16/32-bit,
compressed (ATITC and DXTC, ETC1, S3TC),
NV21_Adreno and V12_Tiled
Note: S3TC/DXTC not enabled due to license issue.
Nonpower-of-two (NPoT) sizes supported

## Slide 27: Adreno features overview (cont.)
Adreno binning architecture
Eliminates unnecessary data traffic to host memory
Improves rendering performance, especially for games, UI, and web applications
Minimizes power consumption
Rendering surface split up into bins Binning creates visibility streams for each triangle
Rendering pass uses visibility streams to draw only pixels that are visible; does not waste GPU cycles and power drawing occluded pixels
Once all pixels for each bin are drawn to an internal tile buffer called GMEM, the GPU efficiently burst writes all pixels to the frame buffer in system memory

## Slide 29: Windows Composition
Composition based window system
Application
Application
Compositor
Multiple application processes render into off-screen, cross-process texture surfaces
Multiple off-screen surfaces are composited to the screen using OpenGL ES for flexible screen layout and transitions
Application
Native OS Window Manager or a Launcher application creating a custom UI experience

## Slide 30: Android Display System: Surface Flinger (HW Composer)
Basic Working Flow
  SurfaceFlinger passes all layers to HW Composer
  HW Composer decides to handle all or part of them, by marking OVERLAY flag.
  Left layers, marked with FB flag, will be handled by SurfaceFlinger.
  HW Composer can let Surfaceflinger clear OVERLAY layers corresponding areas for final composition.
App
App
Surface*
Surface*
Surface
Surface
HW Composer
GPU
Frame Buffer
Overlay Buffer
LCD
Surface Flinger

## Slide 31: Some settings in debugging graphics issues
Setprop debug.egl.hw 0 ; force sw rendering
Setprop debug.sf.hw 0
Setprop debug.composition.type gpu/mdp/c2d/(sw)
Setprop debug.gr.swapinterval 0
Setprop debug.gr.calcfps 1
ls /sys/devices/platform/kgsl-3d0.0/kgsl/kgsl-3d0/

## Slide 32: Q/A
Thank you!

## Slide 33
Back-up Pages

## Slide 34: Khronos Group

## Slide 35: Khronos Standards
Umbrella specification – OpenKOGS plus OS portability
Embedded Media Application APIs
Vector 2D
Streaming Media
Audio
Cross platform desktop 3D
3D Asset Interchange Format
Open Standard Effects Framework
Safety Critical 3D
Embedded 3D
Streaming Media System Integration
Cross platform APIs for window systems
CODEC and media component portability
System Integration APIs
3D APIs
Surface and synch abstraction
Umbrella specification – EGL-based graphics and media stack
3D Authoring

## Slide 36: OpenGL/GLES evolvement

## Slide 37: OpenGL ES 1.1/2.0 and 3.0
OpenGL ES 3.0 new features :
  Transform Feedback, but no Geometry Shader
  Draw Instance, MRT and Occlusion query
  Pixel Buffer Object, Uniform Buffer Object
  More texture formats and sampler type
  New universal compression format ETC2 and ASTC

## Slide 38: Vector Graphics and OpenVG
Standard & API
  OpenVG, SVG, HTML5 Canvas …
  Skia, Cairo, Direct2D …
Target applications
  UI, Browser, Printing, Image Procession …

## Slide 39: EGL and OpenKODE
OpenKODE
  Core OS abstraction
    Main() and Exit()
    Window and Event procession
    IO operations (file, format, socket, …)
    Thread and Synchronization
    Math
  Source code portability
Graphics stack umbrella spec – defines media API and EGL to be present and tests trans-API interoperability
Audio
Embedded 3D
Streaming Media
Vector 2D
Surfaces and synch
Source portability umbrella specification – adds OpenKODE Core OS abstraction API
Native Applications (e.g. Browsers, Games, Navigation, Media)
3D Gaming Engines
TV/Video/Audio Engines
UI/Widget Toolkits
Flash/SVG/Font Engines
EGL
  Encapsualte the difference of different native window system.
  Unified API for context and surface creation and binding
  Cross API integration, resource sharing and synchronization

## Slide 40: OpenCL
OpenCL – Open Computing Language Open, royalty-free standard for programming heterogeneous parallel computing at the intersection of GPU and multi-core CPU capabilities

## Slide 41: WebGL and WebCL
WebGL
  API based on OpenGL ES
  Accessed via JavaScript
  Exposed through HTML5 Canvas
WebCL
  Enable high performance parallel processing on GPU/multicore in web app
  Integrate OpenCL capabilities in JavaScript
  Design with security

## Slide 42: Stream Input & Computer Vision